## Slide 1: Lecture 6: IO Devices

## Slide 2
The Course Organization (Bottom-up)
System Calls (User-level Programming)
Process and CPU Scheduling
Memory Management
Virtualization
Thread
Race Conditions, Lock/Semaphore
Concurrency
IO Devices and Storage
Persistence
File System
HW#4
HW#2
&
Project
HW#3
HW#1

## Slide 3: I/O Devices
I/O is critical for computer systems to interact with IO systems.
Issues :
  How should I/O be integrated into systems?
  What are the general mechanisms?
  How can we make them work efficiently?

## Slide 4: Structure of Input/Output (I/O) Devices
CPU
Memory
Graphics
Prototypical System Architecture
Memory Bus
(proprietary)
General I/O Bus
(e.g., PCI)
Peripheral I/O Bus
(e.g., SCSI, SATA, USB)
CPU and the main memory are attached and communicated via memory bus.
IO devices are connected to the system via a general I/O bus.

## Slide 5: I/O Architecture
Buses
  Data paths that provide to communicate information among CPU(s), RAM, and I/O devices.
I/O bus
  Data path that connects CPU to I/O devices.
  I/O device is connected to I/O bus by three hardware components: I/O ports, interfaces and device controllers.

## Slide 6: Canonical Device
Canonical Devices has two important components.
  Hardware interface allows the system software to control its operation.
  Internals which are implementation specific.
Command
Data
Canonical Device
Registers:
Micro-controller(CPU)
Memory (DRAM or SRAM or both)
Other Hardware-specific Chips
Status
interface
internals

## Slide 7: Hardware Interface of Canonical Device
Status register
  See the current status of the device
Command register
  Tell the device to perform a certain task
Data register
  Pass data to the device, or get data from the device
By reading and writing above three registers,
the operating system can control device behavior.

## Slide 8: Hardware interface of Canonical Device (Cont.)
Typical interaction example
while ( STATUS == BUSY)
; //wait until device is not busy
write data to data register
write command to command register
Doing so starts the device and executes the command
while ( STATUS == BUSY)
; //wait until device is done with your request

## Slide 9: Polling
Operating system waits until the device is ready by repeatedly reading the status register.
  Positive aspect: It is simple and it works.
  However, it wastes CPU time by just waiting for the device.
    Switching to another ready process may better utilize the CPU.
.1 | 1 | 1 | 1 | 1 | p | p | p | p | p | 1 | 1 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization by polling
1 | 1 | 1 | 1 | 1
: task 1
1
: polling
P
“waiting IO”

## Slide 10: Interrupt
Put the I/O request process to sleep and context switch to another.
When the device is finished, wake the process waiting for the I/O by interrupt.
  Positive aspect is to allow CPU and the disk are properly utilized.
1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization by interrupt
1 | 1 | 1 | 1 | 1
: task 1
1
: task 2
2

## Slide 11: Polling vs interrupts
However, “interrupts is not always the best solution”
  If a device performs very quickly, interrupt will “slow down” the system.
  Because context switch is expensive (switching to another process)
If a device is fast  poll is best.
If it is slow  interrupts is better.

## Slide 12: CPU is once again over-burdened
CPU wastes a lot of time to copy a large chunk of data from memory to the device.
1 | 1 | 1 | 1 | C | C | C | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1
CPU
Disk
Diagram of CPU utilization
1 | 1 | 1 | 1 | 1
“over-burdened”
: task 1
1
: task 2
2
C
: copy data from memory

## Slide 13: DMA (Direct Memory Access)
Copy data in memory by knowing “where the data lives in memory, how much data to copy”
When completed, DMA raises an interrupt, and then I/O begins on Disk.
1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1
CPU
DMA
Diagram of CPU utilization by DMA
1 | 1 | 1 | 1 | 1
C | C | C
Disk
: task 1
1
: task 2
2
C
: copy data from memory

## Slide 14: Device interaction
How does the OS communicate with the device?
Solutions
  I/O instructions: a way for the OS to send data to specific device registers.
    Example: in and out instructions on x86
  Memory-mapped I/O
    Device registers available as if they were memory locations.
    The OS utilizes load (to read) or store (to write) to the device instead of main memory.

## Slide 15: Device interaction (Cont.)
How does the OS interact with different specific interfaces?
  Example: We would like to build a file system that worked on top of SCSI disks, IDE disks, USB keychain drivers, and so on.
Solutions: Abstraction
  Abstraction encapsulates any specifics of device interaction.

## Slide 16: File system Abstraction
File system specifics of which disk class it is using.
  Example: It issues block read and write requests to the generic block layer.
The File System Stack
kernel
Application
File System
Generic Block Layer
Device Driver [SCSI, ATA, etc]
Specific Block Interface [protocol-specific read/write]
Generic Block Interface [block read/write]
user
POSIX API [open, read, write, close, etc]

## Slide 17: Problem of File system Abstraction
If there is a device having many special capabilities, these capabilities will go unused in the generic interface layer.
Over 70% of OS code is found in device drivers.
  Any device drivers are needed because you might plug it to your system.
  They are the primary contributor to kernel crashes, making more bugs.

## Slide 18: A Simple IDE Disk Driver
Four types of register
  Control, command block, status and error
  in and out I/O instruction

## Slide 19: A Simple IDE Disk Driver
Control Register:
Address 0x3F6 = 0x08 (0000 1RE0): R=reset, E=0 means "enable interrupt”
Command Block Registers:
    Address 0x1F0 = Data Port
    Address 0x1F1 = Error
    Address 0x1F2 = Sector Count
    Address 0x1F3 = LBA low byte
    Address 0x1F4 = LBA mid byte
    Address 0x1F5 = LBA hi byte
    Address 0x1F6 = 1B1D TOP4LBA: B=LBA, D=drive
    Address 0x1F7 = Command/status

## Slide 20: A Simple IDE Disk Driver
Status Register (Address 0x1F7):
  7 6 5 4 3 2 1 0
  BUSY READY FAULT SEEK DRQ CORR IDDEX ERROR
Error Register (Address 0x1F1): (check when Status ERROR==1)
  7 6 5 4 3 2 1 0
  BBK UNC MC IDNF MCR ABRT T0NF AMNF
  BBK = Bad Block
  UNC = Uncorrectable data error
  MC = Media Changed
  IDNF = ID mark Not Found
  MCR = Media Change Requested
  ABRT = Command aborted
  T0NF = Track 0 Not Found
  AMNF = Address Mark Not Found

## Slide 21: A Simple IDE Disk Driver
Wait for the drive to be ready. Read Status Register (0x1F7) until the drive is not busy and READY.
Write parameters to command registers. Write the sector count, the logical block address (LBA) of the sectors to be accessed, and the drive number (master=0x00 or slave=0x10, as IDE permits just two drives) to command registers (0x1F2-0x1F6).
Start the I/O by issuing read/write to command register. Write READ—WRITE command to command register (0x1F7).
Data transfer (for writes): Wait until the drive status is READY and DRQ (drive request for data); write data to data port.
Handle interrupts. In the simplest case, handle an interrupt for each sector transferred; more complex approaches allow batching and thus one final interrupt when the entire transfer is complete.
Error handling. After each operation, read the status register. If the ERROR bit is on, read the error register for details.

## Slide 22: A Simple IDE Disk Driver
static int ide_wait_ready() {
while (((int r = inb(0x1f7)) & IDE_BSY) ||
!(r & IDE_DRDY))
; // loop until drive isn’t busy
}

## Slide 23: A Simple IDE Disk Driver
static void ide_start_request(struct buf *b) {
  ide_wait_ready();
  outb(0x3f6, 0); // generate interrupt
  outb(0x1f2, 1); // how many sectors?
  outb(0x1f3, b->sector & 0xff); // LBA goes here ...
  outb(0x1f4, (b->sector >> 8) & 0xff); // ... and here
  outb(0x1f5, (b->sector >> 16) & 0xff); // ... and here!
  outb(0x1f6, 0xe0 | ((b->dev&1)<<4) | ((b->sector>>24)&0x0f));
  if(b->flags & B_DIRTY){
    outb(0x1f7, IDE_CMD_WRITE); // this is a WRITE
    outsl(0x1f0, b->data, 512/4); // transfer data too!
  } else {
    outb(0x1f7, IDE_CMD_READ); // this is a READ (no data)
  }
}

## Slide 24: A Simple IDE Disk Driver
void ide_rw(struct buf *b) {
acquire(&ide_lock);
for (struct buf **pp = &ide_queue; *pp; pp=&(*pp)->qnext)
; // walk queue
*pp = b; // add request to end
if (ide_queue == b) // if q is empty
ide_start_request(b); // send req to disk
while ((b->flags & (B_VALID|B_DIRTY)) != B_VALID)
sleep(b, &ide_lock); // wait for completion
release(&ide_lock);
}

## Slide 25: A Simple IDE Disk Driver
void ide_intr() {
struct buf *b;
acquire(&ide_lock);
if (!(b->flags & B_DIRTY) && ide_wait_ready(1) >= 0)
insl(0x1f0, b->data, 512/4); // if READ: get data
b->flags |= B_VALID;
b->flags &= ˜B_DIRTY;
wakeup(b); // wake waiting process
if ((ide_queue = b->qnext) != 0) // start next request
ide_start_request(ide_queue); // (if one exists)
release(&ide_lock);
}

## Slide 26: Summary
IO Devices
  IO system architecture
  General mechanisms
  Device interactions and software development
Next: Virtualizing CPU – Process
  Chapter 4
  Chapter 6